## Slide 1: Tracking nuclei using Keller lab Tgmm software
Afnan Azizi (aa718@cam.ac.uk)
13/12/16

## Slide 2: Cell tracking challenges
Various methods of segmentation and tracking
Large variability in biological samples
Distinguishing various types of behaviour (e.g. movement or division)
Handling of large data sets

## Slide 3: TGMM software workflow
Amat et al. 2015, Nature Protocols

## Slide 4: Image compression
MATLAB script
Compression of images in 5d blocks
Parallelized compression using multiple cores
  Fast read and write
No loss of quality
before
after (x4.5 comp.)

## Slide 5: Image compression
.KLB IMAGES
  Viewable with Fiji

## Slide 6: Fusion, drift correction and normalization
MATLAB scripts
Fusion of up to 4 orthogonal views
  No need for beads or other blob-like features
Image correlation to compute frame-to-frame fluctuations
Estimation of image geometric center to correct long-term drift
Intensity normalization

## Slide 7: TGMM - segmentation
Segmentation using watershed persistence-based agglomeration to create supervoxels
Merging of regions obtained from watershed method
Critical value: 𝜏
Amat et al. 2014, Nature Methods

## Slide 8: TGMM - segmentation
Precompiled binaries for windows (processstack.exe)
Use of CUDA-enabled GPU
Single t-point or time-series
  Visualization of segmentation results
A configuration file to define various parameters

## Slide 9: TGMM - segmentation
𝜏 = 2
𝜏 = 5
𝜏 = 20

## Slide 10
Precompiled binaries for windows (TGMM.exe)
Must use CUDA-enabled GPU
High usage of RAM
Same configuration file as before
Creates xml files containing tracking information for each time point
TGMM - tracking

## Slide 11: Visualization and curation of tracks
MaMuT plugin of Fiji
BigDataViewer import of image data

## Slide 12: Visualization and curation of tracks
Can crop the regions for which tracks are displayed
  MaMuT crashes from too many data points
  Processing tracks and saving can take a long time
Tracks from MaMuT are saved in xml files

## Slide 13: Quality control
Comparison of TGMM generated tracks with manually produced Ground Truth (GT)
  140 tracks over 2 hours

## Slide 14: Curated tracks
Curation is ~3-4 times faster than manual tracking
Track information is stored in easily manipulable xml files
  matlab or other programs for downstream analysis

## Slide 15: Improvements
Choice of GPU to use with TGMM.exe
  Can track multiple movies at the same time
  Requires multiple CUDA-enabled GPUs and very high RAM
Trainable classifier for cell divisions
  GUI based in MATLAB

## Slide 16: Hardware requirements
Multicore CPU (the more cores the better)
CUDA-enabled GPU (the more cores the better)
High amount of RAM
Solid-state drive for faster read and write
3072 CUDA cores

## Slide 17: Thank you
Questions?